## Slide 1
KARNATAKA CLIMATE & ENERGY BASELINE • 2026
Karnataka Sub-National Carbon
Footprint & Emissions Inventory
Sectoral Baselines, Scope 1–3 Breakdown, and a Data-Driven Decarbonization Strategy for South India's Leading Tech & Manufacturing Economy
191,791
sq km
Geographical Area
~61.13M
31 districts
Population Base
25,675+
MW installed
Renewable Capacity (Oct 2025)
+4.10
MMT CO2e/mo
Net Monthly Balance
Assessment spans Scope 1, 2 and 3 emissions across fuel combustion, the electricity grid, water infrastructure, waste management, transport logistics and natural carbon sinks — benchmarked against Karnataka's 25.6 GW renewable fleet, the 4th-largest in India.
Karnataka Carbon Footprint & Emissions Inventory
1

## Slide 2
Thermal Energy, Liquid Fuels & Power Grid Sourcing
PRIMARY EMISSION DRIVERS — SCOPE 1 & SCOPE 2
Direct Thermal — Scope 1
High-Speed Diesel: 679.4k tonnes/month consumed in freight, mining and agriculture.
Petrol: 340.1k tonnes/month across the light-vehicle and two-wheeler fleet.
Combined impact: Drives over 3.21 MMT CO2e/month from mobile logistics and industrial combustion.
Industrial hotspots: Ballari–Hospet mining belt and Peenya/Bidadi manufacturing clusters are the largest point sources.
Electricity Grid Mix — Scope 2
Chart: 
| Coal Thermal (2.45B kWh) | Green Sources (4.45B kWh)
Generation Mix | 2.45 | 4.45
Monthly generation
baseline (B kWh)
64.5% of Karnataka's grid supply already comes from solar, wind and hydro.
25,675+ MW installed renewable capacity statewide as of Oct 2025 (~26,421 MW by Feb 2026) — 4th highest in India.
Grid Carbon Factor: ~0.61 kg CO2e/kWh vs. national avg ~0.82 kg CO2e/kWh — avoiding an estimated 2.71 MMT CO2e every month.
Why it matters: Karnataka's renewable build-out has expanded roughly 5.8x since FY2020 — from ~4,466 MW to over 25,675 MW — making the state grid one of India's cleanest, even as freight and industrial fuel demand keeps Scope 1 emissions elevated.
Karnataka Carbon Footprint & Emissions Inventory
2

## Slide 3
Mobility, Water Pumping & Municipal Waste Emissions
TRANSPORT, HYDROLOGICAL & WASTE DYNAMICS
Transport Fleet
33M+
registered motor vehicles statewide
Public bus transit: 125M km/month
Two-wheelers: 850M km/month
Private cars: 210M km/month
Water Conveyance
90M kWh
power drawn to lift Kaveri basin water
45M cubic metres/month of BWSSB supply
Water lifted ~100+ km & 300+ m elevation to Bengaluru
~54.9k tonnes CO2e/month of indirect emissions
Solid Waste
113k t
landfilled waste generating methane
~85k tonnes CO2e/month from landfill decay
135k tonnes/month diverted to composting
Landfill gas is a short-lived but potent driver
Karnataka Carbon Footprint & Emissions Inventory
3

## Slide 4
Forest Reserve, Ecosystem Storage & Absorption Capacity
TERRESTRIAL CARBON SINK & SEQUESTRATION CANOPY
~1.85 MMT
CO2e absorbed per month by terrestrial biomass — a natural buffer offsetting a major share of the state's direct emissions.
Trend to watch: ISFR 2023 recorded a 459 sq km net decline in Karnataka's forest & tree cover — the 2nd-largest drop of any state, underscoring the need for active canopy protection.
38,730
sq km
Recorded forest cover — 20.2% of state geographical area (Western Ghats / Malenadu core)
549.45M
trees
Statewide tree count outside recorded forest area, incl. agroforestry & urban canopy
580M+
tonnes carbon
Baseline carbon stock held in forest biomass and soil organic carbon pools
Karnataka Carbon Footprint & Emissions Inventory
4

## Slide 5
Actionable Pathways to Net-Zero
STRATEGIC DECARBONIZATION ROADMAP & POLICY PRIORITIES
01
Industrial & Freight Electrification
Shift heavy transport and mining in Ballari–Hospet from diesel to electric drivetrains and green hydrogen; expand PNG city-gas networks and grid-connected EV charging corridors along NH freight routes.
02
Renewable Energy Integration
Scale beyond the current 25,675+ MW solar/wind base with battery storage (2.5 GWh Bidadi BESS plant online) and the 2,000 MW Sharavathi pumped-hydro project to phase out coal for peak demand.
03
Municipal Waste Diversion
Enforce source-segregated, 100% wet-waste diversion to biomethanation and aerobic composting under the Solid Waste Management Rules to eliminate avoidable landfill methane release.
04
Canopy Protection & Restoration
Enforce strict conservation across the Western Ghats Eco-Sensitive Area (which has already lost ~58 sq km of forest since 2013) and expand urban forestry across Greater Bengaluru.
Karnataka Carbon Footprint & Emissions Inventory
5